## Slide 1: Electronics
Sensors

## Slide 2: Sensors
A sensor is a converter that measures a physical quantity and converts it into a signal which can be read by an observer or by an (today mostly) electronic instrument.
For example: our eyes
Light Sensor
Three-axes accelerometer
Ultrasonic Sensor

## Slide 3: Colour
How do we see colour?
When white light falls on an object, it absorbs light of some particular frequencies and reflects the other.
The reflected light is perceived to be of a certain colour.

## Slide 4: Colour sensors
IR Sensors
IR LED emits light
Reflected light received by Phototransistor and converted to voltage.
Higher voltage signifies reflected light of more intensity
LED Sensors
Works on same principle but coloured LEDs used.
Can differentiate better among objects of two different colours but same intensity.
Doubt

## Slide 5: Applications
Rubik’s cube solver
Line follower
Pick and place

## Slide 6: How a line follower works
Array of 5 to 7 color sensors placed in a line.
Objective: Black line must always be in the middle i.e. only the middle sensor must show black
If the immediate left sensor shows black, the robot moves to the left to correct position

## Slide 7: Distance Sensors
Sharp Sensors
Analog distance sensor that uses infrared to detect an object’s distance.
Uses triangulation method
The further the object is
away from the sensor, the
steeper the angle will be
Doubt

## Slide 8
Emitted Light
Reflected Light
Angle calculated
Light detected here
O B J E C T
I R Distance Sensor
doubt

## Slide 9: Ultrasonic Sensors
Sends high frequency sound waves whose echo is received by the receiver.
The time interval between
sending the signal and
receiving echo is calculated
by using a clock pulse
Does not work when the object is of soft, sound absorbing material

## Slide 10: Sharp sensor Vs Ultrasonic sensor
Sharp Sensor
Works on the triangulation method i.e. angle of the light calculated
Gives an analog output that needs to be converted to digital by Analog To Digital Converter
Ultrasonic sensor
Works by using a clock pulse and counting the time pulses between the sent and received signals
Gives a digital output

## Slide 11: Uses of distance sensors
Feature to avoid obstacle
Wall following robots
Easy maneuvering.

## Slide 13: Bump Sensors
Like buttons or switches, bump sensors pull high on a logic pin when pressed.
On being pressed the circuit is completed, hence we get a signal.

## Slide 14
Bump Sensor

## Slide 15: Accelerometer
Used for measuring acceleration of a body.
It can also measure inclination of a body with respect to earth.
Finds many applications in self balancing robots, alarm systems, human motion monitoring, levelling sensor, inclinometer.

## Slide 16: Accelerometer (working)
It comprises a mechanical sensing element and converts the signal from the mechanical to the electrical domain.

## Slide 17: Gyroscope
A gyroscope is a device for measuring or maintaining orientation, based on the principles of angular momentum.
Mechanically, a gyroscope is a spinning wheel or disc in which the axle is free to assume any orientation.

## Slide 18: Gyrometer
A Gyrometer (or gyroscope) is a device for measuring orientation along one or several axis.
It measures the rotation of the robot on the vertical axis to determine its orientation with respect to the arena.
A Gyrometer can be used for several purposes like:
Racing cars
Balancing
Anti roll stabilizers
Ship stabilizer
Computer pointing devices

## Slide 19: Self balancing Robot
Gyrometer or accelerometer used to measure the orientation and acceleration due to gravity
The Gyrometer will tell if the robot is rotating. If it's 0, then the robot is not rotating, that is: it's perfectly still, or going in one direction with some fixed speed keeping balanced. It doesn't say anything about where is up and where is down.
The accelerometer tells if the robot is accelerating forward or backward or any other direction

## Slide 21: Encoder
The encoder is a sensor attached to a rotating object to determine displacement, velocity, or acceleration of a rotating sensor.
As it does not take skidding into consideration, there may be inaccurate readings
It should be very precise as even a small error of few degrees in encoders multiplies over large distances

## Slide 22: Encoders: Working Incremental Measuring System
A Line pattern on glass or plastic disc is made
As these patterns are read a pulse is counted
The signals is analysed by counting up or down with each pulse and stored in digital count.

## Slide 23: Absolute Measuring System
Every position of the measurement is identified by a definite code on a glass or plastic disc.
The code is in the form of light and dark regions within different tracks.
This combination relates to an absolute numerical value.

## Slide 24: Queries?